  O7STRTA Datasheet
Microchirp

One Seven Segment to Rule Them All

1) Features
- It has seven high-performance, low-power LEDs. Duh’.
- It’s bright red! No, like .. really red.
- Advanced RISC architecture. There’s like, only one single-byte command. If that isn’t a reduced instruction set, I don’t know what is.
- Very volatile memory segments. 7/8th of a Byte of RAM.
2) Protocol

The heart of the O7STRTA is a SN74HC164N shift register. It sort-of speaks SPI and it likes either 3.3V or 5V on its VCC pin. One bit is shifted in from the DATA pin with every rising edge on the CLK pin. Each bit is mapped to one segment anode of the display, refer to Section 3) for details. See Listing 1 for example Python code.

3) Segment Mapping

 #!/usr/bin/env python3

 import board
 import time

 # configure spi pins
 spi = board.SPI()
 spi.try_lock()
 spi.configure(1000000)

 # segment mappings
 H = 0b01110110
 E = 0b01111001
 L = 0b00111000
 O = 0b00111111
 _ = 0b00000000

 while True:
   for c in [H, E, L, L, O]:
     spi.write([c])
     time.sleep(0.3)
     spi.write([_])
     time.sleep(0.05)

Each bit of the byte is mapped to a particular
segment anode:

        a
      Ae╶┐┌╴Ad ────
     Af╶┐││┌╴Ac f │ │
    Ag╶┐││││┌╴Ab │ g │ b
       ││││││┌╴Aa ❯❯ ────
    0b·0000000 e │ │
        │ │ c
        ────
        d
4) Pinout

 │ │
 ╰──╁─╁─╁─╁──╯
    ╹ ╹ ╹ ╹

DATA
CLK
GND
VCC
Listing 1: Example Python code for the Adafruit FT232H